## Slide 1
RV32I SoC with an
INT8 AI Accelerator
01
A hardware/software co-design project for FPGA
Eight signed INT8 pairs. One INT32 dot product.
Compare RV32I software with dedicated hardware.
Shiv Sriram
Design & Verification Hackathon 2026
Notes: Project repository: https://github.com/Triumphant-24k/RV32I-Based-SoC-with-an-INT8-AI-Accelerator-on-FPGA
CPU source: https://github.com/Triumphant-24k/riscv-r32-processor-v2 at 64977acc99bfd37eb6c43121e6377a9b47105b72. MIT attribution retained.

## Slide 2
System architecture
02
RV32I processor
32-bit CPU with 32 registers
Executes firmware and controls peripherals
Software multiply uses shifts and adds
Memory and peripherals
16 KiB instruction ROM + 16 KiB data RAM
Memory-mapped INT8 accelerator at 0x40000000
Cycle counter, UART output and status LEDs
Notes: Sources: rtl/cpu_core.v, rtl/soc/ai_soc.sv, rtl/soc/soc_bus.sv, docs/ARCHITECTURE.md. New UART RX extension is in progress and not included in baseline claims.

## Slide 3
How the accelerator works
03
dot(A, B) = sum of A[i] × B[i], for i = 0…7
1. Firmware loads the same two vectors for both paths.
2. The RV32I CPU calculates a software reference.
3. Firmware writes 16 operands and starts the accelerator.
4. Hardware accumulates one product each clock.
5. Firmware reads the result and checks for a match.
8 compute cycles per dot product
Notes: Sources: rtl/soc/int8_accelerator.sv and firmware/main.c. One signed 8x8 multiplier and an INT32 accumulator, processing eight elements sequentially.

## Slide 4
Measured performance in simulation
04
4.81×
End-to-end speedup, example case 0
RV32I software 1,870 cycles 18.70 µs
Accelerator transaction 388 cycles 3.88 µs
Accelerator compute 8 cycles 0.08 µs
Transaction includes input writes, start, polling and result read.
Compute-only speedup: 233.75×. UART time is outside both regions.
Notes: Source: reports/arty_benchmarks.json and reports/arty_uart_sample.txt, baseline board firmware case 0. 1870 / 388 = 4.8196, displayed truncated as 4.81x by firmware. Compute-only: 1870 / 8 = 233.75. Timing assumes target 100 MHz. These are RTL simulation measurements, not physical FPGA observations.

## Slide 5
Verification evidence
05
Existing fixed-vector baseline passed
CPU: 176 directed checks and 300 generated tests
Accelerator: 266 vectors and 12,455 checks
UART: all 256 byte values and 8N1 timing
System: 26 cases in integrated and CPU-only modes
Verilator lint and portable Yosys synthesis passed for the baseline.
Checks cover stalls, reset, MMIO and independent reference results.
Notes: Sources: baseline full regression run before interactive edits on 2026-09-07; reports/regression.txt. Existing baseline passed. The new interactive extension has not passed final regression; first lint attempt identified SYNCASYNCNET in UART RX. Yosys mapping is not Vivado utilization or timing.

## Slide 6
Arty A7-100T demonstration
06
Target: xc7a100tcsg324-1 at 100 MHz
USB-UART: 115200 baud, 8-N-1, no flow control
BTN0 restarts the firmware report
LED0 heartbeat, LED1 busy activity
LED2 PASS, LED3 FAIL
The fixed demo prints 26 comparisons and finishes with ALL PASS.
A successful routed build and a physical board run are still required.
Notes: Sources: boards/arty_a7_100t/arty_a7_top.sv and arty_a7_100t.xdc; docs/ARTY_BRINGUP.md. Pin reference: https://github.com/Digilent/digilent-xdc/blob/master/Arty-A7-100-Master.xdc. Physical validation remains pending.

## Slide 7
Current status and next steps
07
Complete
CPU integration, INT8 accelerator and fixed-vector simulation demo
In progress
UART receive commands and an interactive Windows GUI
Final verification of the new interactive mode
Hardware milestone
Correct Arty build, passing timing, then a measured board demo
Notes: Sources: docs/timing_route.txt, docs/routed.dcp, docs/ai_soc.bit and current interactive work in progress. Supplied old build uses fpga_top and TX D10, with WNS -4.059 ns. Correct Arty flow uses arty_a7_top and TX A9. Do not present the old bitstream as accepted. GUI, serial protocol tests and final interactive regression remain unfinished.